ARES-NAV
Advanced Redundant Estimation System for Aircraft Navigation

Complete Technical Project Specification
Revision 2.5 | March 2026

New in Rev. 2.5: Three aircraft-type-specific home pages (Sailplane / Motorized / UAV GCS) · Profile field 'aircraft_type' and 'cruise_cas_kts' · ISA-based TAS estimation from BMP280 pressure + temperature · Wind triangle computation (WIND EST) · Garmin G1000-style wind arrow + direction + speed on all PFD pages · Wind validity gating (track stability, speed, altitude) · Motorized page layout · UAV GCS page layout · MAVLink placeholder for UAV telemetry

Project	ARES-NAV Avionics & Navigation Platform
Classification	Public Documentation
Developer / Manufacturer	Duwald Systems
MCU 1 — IMU	Arduino Pro Micro (ATmega32U4) | C firmware
MCU 2 — Peripheral	Arduino Pro Micro (ATmega32U4) | C firmware
Home Page Selection	Automatic from profile 'aircraft_type' field
Wind Estimation	ISA TAS (BMP280) + wind triangle — labeled WIND EST
Wind Display	Garmin G1000-style: arrow + direction° + speed kt
Use Cases	Sailplane · Motorized · UAV GCS · Experimental
Status	Experimental / Research Phase

DUWALD SYSTEMS
Experimental Avionics Research

# 1 Abstract
ARES-NAV revision 2.5 introduces three aircraft-type-specific home pages and a physics-based wind estimation system. After profile selection at startup, the system automatically displays the home page appropriate for the active aircraft type — Sailplane Performance Page, Motorized Aircraft PFD, or UAV Ground Control Station Page. The active page is determined by the 'aircraft_type' field in the loaded profile.
Wind direction and speed are estimated on all three pages using the wind triangle method: groundspeed vector from GNSS minus true airspeed vector derived from the profile cruise CAS corrected by ISA atmospheric density (BMP280 pressure and temperature). The result is displayed as a Garmin G1000-style wind arrow with numeric direction and speed, labeled WIND EST to indicate it is an estimate rather than a direct measurement. Wind is only displayed when flight conditions meet stability criteria — straight and level flight at sufficient speed and altitude.

# 2 Revision History
Rev.	Date	Key Changes
1.0	Jan 2026	Initial single-MCU architecture
2.0	Feb 2026	Display screenshots, SPI decision, EKF state vector
2.1	Mar 2026	Dual Arduino Pro Micro split · 14 technical corrections
2.2	Mar 2026	Polyglot language architecture · SQLite schema · Asset strategy
2.3	Mar 2026	Power architecture · Portable enclosure · Dynamic scaling · Nav-Map layers · 9 corrections
2.4	Mar 2026	Aircraft profile system · Yaw confirmation · VNE/Vs tape · Sailplane page
2.5	Mar 2026	Three aircraft-type home pages · ISA TAS estimation · Wind triangle · WIND EST display

# 3 Changes in Revision 2.5
#	Change	Detail
1	'aircraft_type' field added to profile	Mandatory field: 'sailplane' | 'motorized' | 'uav'. Determines the home page shown after startup alignment.
2	'cruise_cas_kts' field added to profile	Typical cruise calibrated airspeed in knots. Used as the TAS base value for wind triangle calculation.
3	ISA TAS estimation from BMP280	TAS derived from profile cruise_cas corrected by atmospheric density ratio √(ρ₀/ρ) using BMP280 pressure and temperature. No pitot required.
4	Wind triangle computation	Wind vector = GNSS groundspeed vector − ISA TAS vector (heading from magnetometer + yaw offset). Updated at 1 Hz when validity criteria met.
5	WIND EST display on all pages	Garmin G1000-style: rotating wind arrow + numeric direction in degrees + speed in knots. Labeled 'WIND EST' always. Shown as '--- / ---' when invalid.
6	Wind validity gating	Wind only computed and displayed when: GS > Vs + 10 kt · Track variance < 5° over 10 s · Altitude > 200 ft AGL · Aircraft type not UAV (UAV wind from MAVLink placeholder)
7	Sailplane home page	Default home page when aircraft_type = 'sailplane'. Performance calculations, glide margin, MacCready. Wind EST in upper-left corner.
8	Motorized home page	Default home page when aircraft_type = 'motorized'. Full PFD layout with GS prominent, attitude, altitude, heading. Wind EST. Engine data panel placeholder.
9	UAV GCS home page	Default home page when aircraft_type = 'uav'. Map dominant left panel, waypoint list, telemetry fields (MAVLink placeholder), small attitude backup indicator.

# 4 Aircraft Profile Schema — Rev. 2.5 Update
Two new mandatory fields are added to the profile JSON in revision 2.5. Existing profiles without these fields will show a 'PROFILE INCOMPLETE' warning and default to the standard PFD page.

✦ Change in Rev. 2.5 — Rev. 2.5: 'aircraft_type' and 'cruise_cas_kts' added as mandatory profile fields. Existing profiles must be updated.

## 4.1 Complete Profile Schema
Field	JSON Key	Type	Required	Description
Aircraft name	aircraft_name	string	Yes	Full aircraft type designation
Pilot callsign	callsign	string	Yes	Shown in PFD header
Aircraft type	aircraft_type	string	Yes	'sailplane' | 'motorized' | 'uav' — determines home page
Cruise CAS	cruise_cas_kts	number	Yes	Typical cruise calibrated airspeed in knots — used for TAS/wind estimate
VNE	v_ne_kts	number	Yes	Never-Exceed Speed in knots — red line on speed tape
Stall speed	v_s_kts	number	Yes	Stall speed in knots — stall warning threshold
Best-glide speed	v_bg_kts	number	Yes	Best L/D speed in knots — green triangle on speed tape
Polar a	polar_a	number	Sailplane only	Quadratic polar coefficient (m/s per (m/s)²)
Polar b	polar_b	number	Sailplane only	Linear polar coefficient
Polar c	polar_c	number	Sailplane only	Constant polar offset — minimum sink

## 4.2 Updated Example Profiles
ASK-21 — profiles/ask21.json (sailplane)
{
"aircraft_name": "Schleicher ASK-21",
"callsign": "D-KABC",
"aircraft_type": "sailplane",
"cruise_cas_kts": 52,
"v_ne_kts": 135,
"v_s_kts": 38,
"v_bg_kts": 52,
"polar_a": 0.00150,
"polar_b": -0.05200,
"polar_c": 1.92000
}

Generic Motor-Glider — profiles/motorglider.json (motorized)
{
"aircraft_name": "Generic Motor-Glider",
"callsign": "D-MXYZ",
"aircraft_type": "motorized",
"cruise_cas_kts": 90,
"v_ne_kts": 150,
"v_s_kts": 52,
"v_bg_kts": 75,
"polar_a": 0.0,
"polar_b": 0.0,
"polar_c": 0.0
}

UAV Ground Control Station — profiles/uav_gcs.json (uav)
{
"aircraft_name": "UAV Ground Control Station",
"callsign": "GCS-01",
"aircraft_type": "uav",
"cruise_cas_kts": 0,
"v_ne_kts": 999,
"v_s_kts": 0,
"v_bg_kts": 0,
"polar_a": 0.0,
"polar_b": 0.0,
"polar_c": 0.0
}
ℹ Note — For UAV profiles, polar and speed fields are set to zero/999. Speed tape warnings and sailplane calculations are suppressed when aircraft_type = 'uav'. Wind EST is also suppressed — UAV wind data comes from the MAVLink telemetry placeholder (§8.3).

# 5 Wind Estimation System (WIND EST)
ARES-NAV estimates wind direction and speed using the wind triangle method. Because there is no pitot sensor, True Airspeed (TAS) is derived from the aircraft's profile cruise CAS corrected by the ISA atmospheric density ratio computed from BMP280 measurements. The result is physically meaningful but labeled 'WIND EST' throughout the system to clearly distinguish it from a direct measurement.

## 5.1 ISA TAS Estimation
The International Standard Atmosphere (ISA) defines air density as a function of pressure and temperature. BMP280 measures both. TAS is the speed through the air mass — it equals CAS multiplied by the square root of the sea-level-to-current density ratio:
# Inputs from BMP280 (MCU 2 peripheral frame):
pressure_pa = bmp280_pressure_hpa * 100.0
temp_kelvin = bmp280_temperature_celsius + 273.15

# ISA air density at current altitude (ideal gas law):
R_air = 287.05 # J/(kg·K) — gas constant dry air
rho = pressure_pa / (R_air * temp_kelvin) # kg/m³
rho_0 = 1.225 # kg/m³ — ISA sea level density

# TAS from profile cruise CAS:
cas_ms = profile.cruise_cas_kts * 0.5144 # knots → m/s
tas_ms = cas_ms * sqrt(rho_0 / rho) # ISA TAS correction

Parameter	Value / Detail
Typical accuracy	±3–5 kt at altitudes below 10,000 ft — sufficient for pilot situational awareness
Accuracy degradation	Increases if actual cruise speed differs from profile cruise_cas_kts (e.g. during climb, descent, or abnormal speeds)
Temperature sensitivity	1°C error → ~0.17% TAS error at low altitude — negligible
Pressure sensitivity	1 hPa error → ~0.4% TAS error — acceptable
BMP280 update rate	26 Hz — TAS updated every frame, wind averaged over 10 s

## 5.2 Wind Triangle Computation
With TAS known, the wind vector is computed as the vector difference between the GNSS groundspeed vector and the TAS vector:
import math

# Groundspeed vector (from GNSS — MCU 2 frame):
gs_ms = gnss_groundspeed_cms / 100.0
track_r = math.radians(gnss_track_deg)
gs_north = gs_ms * math.cos(track_r)
gs_east = gs_ms * math.sin(track_r)

# TAS vector (from magnetometer heading + yaw offset):
hdg_r = math.radians(mag_heading_deg + yaw_offset_deg)
tas_north = tas_ms * math.cos(hdg_r)
tas_east = tas_ms * math.sin(hdg_r)

# Wind vector:
w_north = gs_north - tas_north
w_east = gs_east - tas_east

wind_speed_ms = math.sqrt(w_north**2 + w_east**2)
wind_speed_kts = wind_speed_ms / 0.5144
wind_dir_deg = (math.degrees(math.atan2(w_east, w_north)) + 360) % 360
# Wind direction = direction FROM which wind blows (meteorological convention):
wind_from_deg = (wind_dir_deg + 180) % 360

Future option — Pitot tube module (MCU 3): A third Arduino Pro Micro (MCU 3) with two BMP280 sensors (0x76 = static pressure in housing, 0x77 = total pressure in pitot tube) can replace the WIND EST estimation with true IAS and real measured wind. The pitot module is optional and hot-pluggable — ARES-NAV automatically detects presence via /dev/aresnav-pitot and switches from WIND EST to WIND. See Design Constraints §18 for implementation notes. / ⚠ Warning — WIND EST accuracy depends entirely on the assumption that the aircraft is flying at profile cruise_cas_kts. During climbs, descents, turns, or off-cruise speeds, the estimate will be wrong. Always cross-check against known weather information. Never use WIND EST for navigation decisions without independent wind data.

## 5.3 Wind Validity Gating
Wind is only computed and displayed when all five conditions are met simultaneously. If any condition fails, the display shows '--- / ---kt' and the arrow is hidden:
Condition	Threshold	Reason
Groundspeed	GS > (v_s_kts + 10 kt)	Below this speed the aircraft may be stalling — GS vector unreliable
Track stability	Track variance < 5° over last 10 s (rolling window)	Turns corrupt the wind triangle — straight flight required
Altitude AGL	Altitude > 200 ft AGL (from SRTM lookup at current position)	Ground effect and turbulence near ground make estimate unreliable
Aircraft type	aircraft_type ≠ 'uav'	UAV GCS uses MAVLink placeholder — ground-based, no wind triangle
Yaw alignment	Yaw offset confirmed by pilot at startup	Unconfirmed heading offset would corrupt TAS vector direction

When all conditions are met, the wind estimate is updated at 1 Hz. A 10-second exponential moving average (α = 0.1 per second) is applied to both wind_speed and wind_from_deg to reduce display jitter. The averaging uses circular mean for the direction to handle the 360°/0° wrap correctly.

## 5.4 Wind Display — Garmin G1000 Style
The wind indicator is rendered in the upper-left area of every home page. It consists of three elements drawn by the rendering engine each frame:
- Wind arrow — a rotating arrow pointing FROM the wind direction. Arrow length is proportional to wind speed (minimum length at 3 kt, maximum at 40 kt). Rendered as a QPainter arrow centred in a small circular area (~60×60 px scaled).
- Direction — numeric magnetic direction in degrees from which the wind blows, right-aligned below the arrow circle. Format: '270°M'
- Speed — wind speed in knots below the direction. Format: '12 kt'
- Label — 'WIND EST' in small text above the arrow, always visible, colored amber to distinguish from a measured value

Parameter	Value / Detail
Position on screen	Upper-left corner, above and left of the attitude indicator
Arrow colour	White when valid, gray when below thresholds
Direction convention	Meteorological — FROM which the wind blows (270° = wind from west = tailwind on heading 090°)
Speed units	Knots — consistent with all other speed values in ARES-NAV
Calm wind	When wind_speed < 3 kt: arrow hidden, display shows 'CALM'
Update rate	1 Hz (10 s EMA applied)
Invalid state	Arrow hidden, '--- / --- kt', label 'WIND EST' remains in amber

# 6 Home Page Selection
The home page is the first page displayed after the startup sequence completes. It is determined automatically from the 'aircraft_type' field of the loaded profile. No pilot input is required — the correct page loads immediately.

Profile aircraft_type	Home Page	Description
sailplane	Sailplane Performance Page	MacCready, glide margin, best-glide speed indicator, wind EST
motorized	Motorized Aircraft PFD	Full PFD with GS prominent, attitude, altitude, heading, wind EST, engine placeholder
uav	UAV GCS Page	Map dominant, waypoint list, telemetry fields, small attitude backup, MAVLink placeholder
(field missing or invalid)	Standard PFD	Fallback — 'PROFILE INCOMPLETE' banner shown

Page navigation via long-press encoder cycles through all available pages regardless of home page. The home page is always the first in the cycle.

# 7 Sailplane Home Page (aircraft_type: sailplane)
The sailplane home page is optimised for soaring flight. It emphasises the performance calculations derived from the active profile polar, the glide margin to the active waypoint, and wind estimation. The built-in aircraft variometer handles vertical speed — ARES-NAV does not duplicate this.

Sailplane Home Page — Layout
┌─────────────────────────────────────────────────────────────┐
│ WIND EST ↖ 270°M / 12kt D-KABC / ASK-21 [LNAV] │
├──────────────┬──────────────────────────────┬───────────────┤
│ Glide │ │ Next WP │
│ Current L/D │ Attitude Indicator │ EDHI 38nm │
│ 28.4 │ (full size, centred) │ Bearing 275° │
│ │ │ │
│ Required │ │ Glide Margin │
│ L/D to WP │ │ ████░░░ +4.2 │
│ 24.1 │ │ │
├──────────────┴──────────────────────────────┴───────────────┤
│ GS: 94 kt Alt: 4250 ft MC: 2.0 Heading: 093°M │
└─────────────────────────────────────────────────────────────┘

## 7.1 Displayed Elements
Element	Position	Data Source	Update
WIND EST arrow + dir + speed	Top-left	Wind triangle (§5)	1 Hz
Profile callsign + aircraft	Top-right header	Active profile	Static
LNAV / FD annunciators	Top-right header	EKF nav state	10 Hz
Current L/D (glide ratio)	Left panel — top	GS / polar sink at GS, 5 s avg	1 Hz
Required L/D to waypoint	Left panel — bottom	(alt − WP_elev) / dist_to_WP	1 Hz
Attitude indicator	Centre — full size	EKF quaternion	60 Hz
Next waypoint name + distance	Right panel — top	Nav DB + EKF position	1 Hz
Bearing to waypoint	Right panel	WMM-corrected magnetic bearing	1 Hz
Glide margin bar	Right panel — bottom	Current L/D − Required L/D	1 Hz
Groundspeed	Bottom bar	GNSS	10 Hz
QNH Altitude	Bottom bar	BMP280 + QNH	26 Hz
MacCready value	Bottom bar	Pilot-set, encoder on this page	On change
Magnetic heading	Bottom bar	EKF + WMM	10 Hz

## 7.2 Glide Margin Bar
The glide margin bar is the primary decision-making indicator on the sailplane page. It is centred at zero, extends right (green) for positive margin and left (red) for negative margin:
glide_margin = current_LD - required_LD_to_waypoint
# Positive = can make the waypoint at current glide performance
# Negative = cannot make the waypoint — land or find a thermal
# Bar scale: ±10 L/D units full deflection

# 8 Motorized Aircraft Home Page (aircraft_type: motorized)
The motorized home page is a full Primary Flight Display with groundspeed shown prominently as the primary speed reference. There is no airspeed tape — groundspeed is displayed as a large numeric value. This page suits motor-gliders, motorized ultralight aircraft, and experimental aircraft where GNSS groundspeed is the primary speed reference.

✦ Change in Rev. 2.5 — Rev. 2.5: Motorized home page introduced. Replaces the generic PFD as the first page for motorized profiles. Key difference: GS prominent as large numeral instead of airspeed tape.

Motorized Home Page — Layout
┌─────────────────────────────────────────────────────────────┐
│ WIND EST ↙ 045°M / 8kt D-MXYZ / Motor-Gl [FD] │
├──────────┬──────────────────────────────────────┬───────────┤
│ │ │ ALT │
│ GS │ │ 3 2 5 0 │
│ 9 4 kt │ Attitude Indicator │ ft │
│ (large) │ (full size, centred) │ │
│ │ │ VS │
│ HDG │ │ +350 │
│ 093°M │ │ ft/min │
├──────────┴──────────────────────────────────────┴───────────┤
│ QNH: 1013 hPa │ Next WP: EDHI 38nm 275° │ ETA: 00:24 │
├─────────────────────────────────────────────────────────── ┤
│ ENGINE RPM: ---- CHT: ----°C EGT: ----°C [Phase 5] │
└─────────────────────────────────────────────────────────────┘

## 8.1 Displayed Elements
Element	Position	Source	Notes
WIND EST	Top-left	Wind triangle (§5)	Same as all pages
Callsign + aircraft	Top-right	Active profile
Groundspeed (large numeral)	Left panel	GNSS	Primary speed reference — no tape
Magnetic heading	Left panel below GS	EKF + WMM
Attitude indicator	Centre	EKF quaternion	Full size
QNH Altitude (numeric)	Right panel	BMP280 + QNH	No tape — numeric only
Vertical speed	Right panel below alt	BMP280 derivative	ft/min
QNH value	Bottom bar	Pilot-set	Adjustable via encoder
Next waypoint + distance + bearing	Bottom bar	Nav DB + EKF
ETA to waypoint	Bottom bar	Distance / GS	GS-ETA, labeled
Engine data panel	Bottom strip	Placeholder — Phase 5	RPM, CHT, EGT shown as '----'

## 8.2 Engine Data Panel — Phase 5 Placeholder
The bottom strip of the motorized page reserves space for engine instrumentation. In Rev. 2.5 all values display as '----'. The panel is designed to accept data from a future engine monitor connected via UART or USB in Phase 5. The fields are:
- RPM — engine speed in revolutions per minute
- CHT — Cylinder Head Temperature in °C
- EGT — Exhaust Gas Temperature in °C
- OIL — Oil temperature in °C (optional field)
The engine data panel is hidden entirely when aircraft_type = 'sailplane' or 'uav'.

# 9 UAV Ground Control Station Page (aircraft_type: uav)
The UAV GCS page is designed for operating unmanned aircraft from a ground station. The map is the primary element, occupying the left 60% of the display. The right panel provides waypoint navigation, UAV telemetry status, and a small attitude indicator as a backup reference for the UAV's attitude.

⚠ Warning — ARES-NAV is a navigation display system — it does not have a radio data link to the UAV. The telemetry fields (Battery %, Signal, Flight Mode) on this page are placeholders for data that would arrive via a MAVLink-over-UDP interface in Phase 5. In Rev. 2.5 all telemetry fields display as '---'. The attitude indicator on this page shows the ARES-NAV unit's own attitude (at the ground station), not the UAV's attitude.

✦ Change in Rev. 2.5 — Rev. 2.5: UAV GCS page introduced. Telemetry fields are Phase 5 placeholders. Attitude indicator shows GCS unit orientation (IMU-derived), not UAV attitude.

UAV GCS Home Page — Layout
┌─────────────────────────────────────────────────────────────┐
│ GCS-01 MAVLink: NOT CONNECTED│
├─────────────────────────────┬───────────────────────────────┤
│ │ NEXT WAYPOINT │
│ │ WP3 — SOLDO │
│ Moving Map │ Bearing: 086°M Dist: 22nm │
│ (60% display width) │ ETA GS: 00:14 │
│ North-up ├───────────────────────────────┤
│ Own-ship symbol │ WAYPOINT LIST │
│ Flight plan route │ ▶ WP3 086° 22.4nm │
│ Airport symbols │ WP4 112° 38.1nm │
│ Airspace overlay │ EDXB 098° 50.2nm │
│ ├───────────────────────────────┤
│ │ TELEMETRY [Phase 5] │
│ │ Batt: --- % │
├──────────────┬──────────────┤ Signal: --- │
│ Attitude │ GS: --- kt │ Mode: --- │
│ (small) │ Alt: --- ft ├───────────────────────────────┤
│ GCS unit │ Hdg: ---°M │ SRTM TERRAIN [colour layer] │
└──────────────┴──────────────┴───────────────────────────────┘

## 9.1 Displayed Elements
Element	Position	Source	Notes
MAVLink connection status	Top-right header	MAVLink interface (Phase 5)	'NOT CONNECTED' in Rev. 2.5
Moving map	Left 60% — full height	OpenAIP SQLite + SRTM	North-up, all layers active
Airport symbols on map	Left panel	OpenAIP R*Tree query	Nearest airports in viewport
Airspace on map	Left panel	OpenAIP polygon query	Class D/C/danger overlaid
Terrain colour	Left panel — bottom layer	SRTM + EGPWS colour scale	Relative to GCS altitude (not UAV)
Next waypoint name + bearing + distance	Right panel — top	Nav DB + EKF position	Active waypoint from flight plan
ETA to next waypoint	Right panel — top	Distance / GS	GS-ETA
Waypoint list	Right panel — middle	Flight plan	Active WP marked with ▶
Battery %	Right panel — telemetry	MAVLink (Phase 5)	'---' in Rev. 2.5
Signal strength	Right panel — telemetry	MAVLink (Phase 5)	'---' in Rev. 2.5
Flight mode	Right panel — telemetry	MAVLink (Phase 5)	'---' in Rev. 2.5
Attitude indicator (small)	Bottom-left	EKF — GCS unit attitude	Shows GCS unit orientation, NOT UAV
Groundspeed	Bottom-left below attitude	GNSS	GCS unit groundspeed — 0 when static
Altitude	Bottom-left	BMP280 + QNH	GCS unit altitude
Heading	Bottom-left	EKF + WMM	GCS unit heading

## 9.2 MAVLink Interface — Phase 5 Specification
In Phase 5, UAV telemetry will be received via MAVLink protocol over UDP on the Pi's network interface. The interface specification for future implementation:
Protocol: MAVLink v2
Transport: UDP — Pi listens on 0.0.0.0:14550 (standard GCS port)
Source: UAV companion computer or flight controller telemetry radio
Messages used:
  HEARTBEAT (id 0) — MAVLink connection + flight mode
  SYS_STATUS (id 1) — battery voltage + remaining %
  GLOBAL_POSITION_INT (id 33) — UAV position (not used for ARES-NAV nav)
  RADIO_STATUS (id 109) — signal RSSI
Python library: pymavlink (pip install pymavlink)
Thread: separate MAVLink listener thread, nice +5
Timeout: 5 s no HEARTBEAT → 'NOT CONNECTED' shown

# 10 Standard PFD Pages (accessible from all profiles)
All three aircraft types can access the standard PFD pages via long-press encoder navigation. These pages are identical regardless of profile type, with the exception that speed tape markings are always sourced from the active profile.

## 10.1 Standard PFD

Figure 1 — Standard PFD (accessible from all profile types via long-press)
Wind EST indicator is shown in the upper-left corner of the standard PFD in the same position as on all home pages. The speed tape uses profile VNE, Vs, and v_bg markings. Callsign is shown in the top-right status bar.

## 10.2 PFD with Flight Director

Figure 2 — PFD with Flight Director active
## 10.3 Fault Page

Figure 3 — Fault and Master Caution page
## 10.4 Navigation Map

Figure 4 — Navigation Map with terrain, airspace, and airport layers
## 10.5 GPS Status

Figure 5 — GPS Status Page

# 11 Startup Sequence

Figure 6 — Phase 1: Color bar self-test

Figure 7 — Phase 2: INS alignment with live GNSS status
Phase	Duration	Events
1 — Display self-test	~3 s	Full-screen color bars
2 — Power check	~1 s	Battery + bus voltage — BATT LOW if < 10.5V
3 — INS alignment	60 s	Gravity · GNSS lock · AK8963 · Temp cal · EKF init · Live GNSS at splash bottom
4 — Yaw alignment	Pilot	Magnetometer heading shown · Encoder adjusts offset · Short-press confirms
5 — Profile selection	Pilot	Profile list shown · Encoder scrolls · Short-press selects · Skipped if 1 profile
6 — Nav DB + wind init	~1 s	SQLite load · SRTM index · Wind system initialised (awaiting validity conditions)
7 — Home page	Automatic	Home page from aircraft_type field loaded · EKF running · 60 Hz render

# 12 Fault Detection
Parameter	Fault	Annunciation	Degraded Mode
IMU 1/2/3	CRC fail / 3 missed frames	IMU x FAIL	Remaining 2 continue
Magnetometer 1/2/3	AK8963 not responding	MAG x FAIL	Heading from remaining MAGs
GNSS	No 3D fix	GPS LOST	DR 3–10 nm/min
Barometer	NACK / out-of-range	BARO FAIL	GNSS geometric altitude; TAS/wind suppressed
MCU 1 USB	No frame > 500 ms	MCU1 LINK	EKF stopped
MCU 2 USB	No frame > 500 ms	MCU2 LINK	No GNSS/baro/wind
EKF state	Quaternion / velocity bounds	ATTITUDE DEGRADED	EKF re-init
Yaw alignment	Not confirmed	HDG UNCONFIRMED	Wind EST suppressed (heading needed)
Profile	Missing / invalid JSON	PROFILE INCOMPLETE	Standard PFD, no speed limits
Wind validity	Gating conditions not met	WIND EST shows '---'	Wind suppressed only
Battery	< 10.5V	BATT LOW	Alert
Battery critical	< 9.3V	BATT CRITICAL	Graceful shutdown
Overspeed	GS > v_ne_kts	OVERSPD (flashing)	Warning
Stall	GS < v_s_kts	STALL (flashing)	Warning
MAVLink (UAV)	No heartbeat > 5 s	MAVLink: NOT CONNECTED	Telemetry fields show '---'

# 13 MCU Firmware (C — Arduino Pro Micro ATmega32U4)
## 13.1 MCU 1 — IMU Controller
Parameter	Value / Detail
USB Serial Number in descriptor	ARESNAV-IMU
Pi device symlink	/dev/aresnav-imu (udev rule)
SPI clock	8 MHz — SPISettings(8000000, MSBFIRST, SPI_MODE0)
Sample rate	500 Hz — Timer1 COMPA ISR
Timestamp	uint64 via Timer1 overflow counter + cli()/sei() atomic read
Frame	62 bytes — sync, uint64 ts, 3× gyro+accel, mag median, temp, faults, CRC8
SRAM budget	1272 / 2560 bytes (50% headroom)
Watchdog	wdt_enable(WDTO_2S)

## 13.2 MCU 2 — Peripheral Controller
Parameter	Value / Detail
USB Serial Number in descriptor	ARESNAV-PERI
Pi device symlink	/dev/aresnav-peri (udev rule)
GNSS	NEO-M8N on Serial1 at 115200 baud, 10 Hz
Barometer	BMP280 on I²C, 26 Hz — pressure + temperature (temperature used for ISA TAS)
Encoder	GPIO interrupt ISR — delta accumulated, button flags on press
Frame	48 bytes — sync, uint64 ts, lat, lon, alt, GS, track, pressure, temp, fix, sats, HDOP, encoder, button, battery, CRC8
Watchdog	wdt_enable(WDTO_2S)

## 13.3 uint64 Timer and Encoder ISR
// MCU 1+2 — uint64 timestamp via Timer1 overflow:
volatile uint32_t t1_ovf = 0;
ISR(TIMER1_OVF_vect) { t1_ovf++; }
uint64_t micros64(void) {
    uint8_t sreg=SREG; cli();
    uint32_t ovf=t1_ovf, tcnt=TCNT1;
    SREG=sreg;
    return ((uint64_t)ovf<<15)|(tcnt>>1);
}

// MCU 2 — Encoder ISR:
volatile int8_t enc_delta=0;
void enc_isr(void) {
    uint8_t clk=digitalRead(ENC_CLK), dt=digitalRead(ENC_DT);
    if(clk!=last_clk){ enc_delta+=(clk==dt)?+1:-1; last_clk=clk; }
}

# 14 EKF Sensor Fusion (Python + numpy)
Parameter	Value / Detail
State	17: NED pos (m), NED vel (m/s), quaternion, gyro bias (rad/s), accel bias (m/s²)
Prediction	500 Hz from MCU 1
Correction	10 Hz GNSS + 26 Hz baro from MCU 2
Coordinate frame	Local NED metres — lon factor cos(lat)×111320 updated every 60 s
Temperature comp.	bias_corrected = bias_cal + k_T × (T_now − T_cal) per axis
Magnetic decl.	WMM2025 — updated every 60 s from GNSS position
Yaw offset	Applied to heading output after pilot confirmation at startup
NaN guard	CRC8 → np.isfinite() → state sanity (3 layers)
Wind inputs from EKF	mag_heading_deg + yaw_offset_deg → wind triangle (§5.2)
ISA inputs from MCU 2	bmp280_pressure_hpa + bmp280_temperature_celsius → TAS (§5.1)

# 15 Software Architecture
## 15.1 Language Assignment
Component	Language	Notes
MCU 1 + MCU 2 firmware	C (avr-gcc / Arduino)	Bare-metal, ISR, direct register access
EKF sensor fusion	Python + numpy	BLAS matrix ops, GIL released, ~12 µs/prediction
Wind estimation	Python + math	1 Hz update, circular mean for direction averaging
ISA TAS computation	Python + math	Per MCU 2 frame — negligible compute
PFD + all page rendering	Python + PyQt5	60 Hz, QPainter CPU rasterization
Profile system	Python + json	Loaded at startup, validated, cached in memory
Navigation database	Python + SQLite	R*Tree spatial index, async queries
Terrain processing	Python + numpy + cv2	memmap .hgt tiles, bilinear resize
MAVLink (Phase 5)	Python + pymavlink	UDP listener thread, not implemented in Rev. 2.5

## 15.2 Thread Structure
Thread	Rate	Priority
USB Reader A — MCU 1	500 Hz	nice −10
USB Reader B — MCU 2	10 Hz	nice −5
EKF prediction	500 Hz	nice −10
EKF correction	10 Hz	nice −10
Wind estimator	1 Hz	nice 0
PFD render (Qt main)	60 Hz	Qt normal
Nav DB queries	On demand	nice +5
SRTM tile loader	On position change	nice +5
Power monitor	1 Hz	nice 0
MAVLink listener (Phase 5)	Async UDP	nice +5

# 16 File System Layout
/boot/ares-nav/
  profiles/
    ask21.json ← Schleicher ASK-21 (sailplane)
    discus2c.json ← Schempp-Hirth Discus-2c (sailplane)
    motorglider.json ← Generic motor-glider (motorized)
    uav_gcs.json ← UAV ground control station (uav)
    <any_name>.json ← Additional profiles
  nav.db ← OpenAIP SQLite + R*Tree
  srtm/ ← NASA SRTM .hgt tiles
  wmm2025.json ← Magnetic declination model
  imu_cal.json ← IMU temperature compensation coefficients
  config.json ← BMP280 address, QNH units, display prefs
  state.json ← Last QNH, yaw offset, last profile, last position
  assets/
    horizon_base.png ← Sky/ground gradient (QTransform per frame)
    bank_arc.png ← Bank angle arc ring (static blit)
    aircraft_symbol.png ← Centre aircraft symbol (static blit)
    logo.png ← Splash screen logo

# 17 Development Roadmap
Phase	Title	Key Deliverables	Status
1	Concept	Architecture, mockups, component selection	Complete
2	Experimental Platform	MCU 1+2 C firmware (uint64, ISR encoder, USB serial IDs), basic PyQt5 PFD	In Progress
3	Navigation Core	EKF (17-state NED), GNSS fusion, baro alt, profile system, yaw alignment, ISA TAS, wind triangle	Planned
4	Full Interface	Three home pages, dynamic-scaling, Nav-Map layers, all startup phases, speed tape markings	Planned
5	Extended Research	MAVLink UAV telemetry, engine monitor UART, ADS-B RTL-SDR, autopilot stub · Optional: MCU 3 Pitot module (IAS + real wind, 2x BMP280)	Future

# 18 Design Constraints and Decision Log
Constraint / Decision	Outcome	Rev.
3× IMU I²C address collision	SPI 3× CS pins on MCU 1	2.0
Single MCU timing conflict	Dual Arduino Pro Micro	2.1
SPI clock unspecified	8 MHz explicit	2.1
uint32 timestamp overflow	uint64 via Timer1 overflow ISR	2.1→2.3
GNSS baud 9600 insufficient	115200 on MCU 2	2.1
EKF state in lat/lon degrees	NED metres, 17-state	2.1
No magnetic declination	WMM2025 every 60 s	2.1
IMU temperature drift	Linear compensation from BMP280 temp	2.1
No watchdog	HW watchdog both MCUs + systemd + EKF thread watchdog	2.1
NaN propagation	CRC + isfinite + sanity (3 layers)	2.1
DR accuracy overstated	Corrected to 3–10 nm/min (consumer MEMS)	2.1
Nav DB on USB	Permanent on microSD; USB = flight plans only	2.1
QNH resets on power cycle	state.json persistence	2.1
PyQt5 GPU claim incorrect	QPainter = CPU rasterization	2.3
Asset strategy incorrect	Horizon texture = PNG + QTransform; pitch ladder = code	2.3
Encoder polled at 10 Hz	GPIO interrupt ISR on MCU 2	2.3
Flat-Earth lon factor set once	Recomputed every 60 s from current lat	2.3
USB auto-mount headless	udev + systemd mount, label ARESNAV-PLANS	2.3
ttyACM order non-deterministic	USB serial numbers + udev symlinks	2.3
Variometer in ARES-NAV	Removed — aircraft has one already	2.4
Yaw alignment automatic	Manual encoder confirmation	2.4
Single aircraft config	Multi-profile JSON system in /boot/ares-nav/profiles/	2.4
No wind without pitot	ISA TAS from BMP280 + wind triangle — labeled WIND EST	2.5
Wind display format	Garmin G1000 style: rotating arrow + dir° + speed kt	2.5
Single generic home page	Three type-specific home pages from profile aircraft_type	2.5
Home page type detection	Manual field 'aircraft_type' in profile JSON — no auto-detection	2.5
UAV telemetry	MAVLink Phase 5 placeholder — '---' fields in Rev. 2.5	2.5
Engine data	Phase 5 placeholder panel on motorized page — '----' in Rev. 2.5	2.5
No SVS / 3D terrain	Excluded — GPU context conflict, Phase 5 review	2.1
Pitot tube IAS / real wind — optional future extension	MCU 3 (Arduino Pro Micro) + 2x BMP280 (0x76 static housing, 0x77 pitot total pressure). Hot-plug optional module. Replaces WIND EST with true IAS and real wind when connected.	2.6

# 19 Glossary
Term	Definition
ARES-NAV	Advanced Redundant Estimation System for Aircraft Navigation
EKF	Extended Kalman Filter — optimal state estimator for nonlinear systems
NED	North-East-Down — local Cartesian coordinate frame in metres
GNSS	Global Navigation Satellite System — GPS, GLONASS, Galileo, BeiDou
GS	Groundspeed — GNSS-derived speed over ground (not IAS or TAS)
IAS	Indicated Airspeed — measured by pitot tube (not available in ARES-NAV)
CAS	Calibrated Airspeed — IAS corrected for position error
TAS	True Airspeed — CAS corrected for air density. Estimated from ISA in ARES-NAV.
ISA	International Standard Atmosphere — density/pressure/temperature model
WIND EST	Wind Estimated — wind derived from wind triangle, not direct measurement
IMU	Inertial Measurement Unit — accelerometer, gyroscope, magnetometer
MCU 1	Arduino Pro Micro #1 — IMU SPI controller (ATmega32U4, C firmware)
MCU 2	Arduino Pro Micro #2 — Peripheral controller (ATmega32U4, C firmware)
WMM2025	World Magnetic Model 2025 — magnetic declination (NOAA)
BMS	Battery Management System — LiPo protection and balancing
VNE	Never-Exceed Speed from aircraft profile — red line on speed tape
Vs	Stall Speed from aircraft profile — stall warning threshold
v_bg	Best-Glide Speed from aircraft profile — green triangle on speed tape
cruise_cas_kts	Profile cruise CAS — TAS base value for wind triangle
aircraft_type	Profile field: 'sailplane' | 'motorized' | 'uav' — selects home page
L/D	Lift-to-Drag ratio (glide ratio)
MC	MacCready value — pilot-set expected thermal strength
MAVLink	UAV communication protocol — Phase 5 data link for UAV telemetry
XTK	Cross-Track Error — lateral deviation from route centreline
RAIM	Receiver Autonomous Integrity Monitoring — GNSS integrity check
SRTM	Shuttle Radar Topography Mission — NASA 30 m elevation dataset
ISR	Interrupt Service Routine — hardware callback in C firmware
CRC8	8-bit Cyclic Redundancy Check (polynomial 0x07)
QTransform	Qt matrix transform for asset rotation/translation per frame
R*Tree	Spatial index in SQLite for geographic bounding-box queries
avr-gcc	GNU Compiler Collection for AVR (ATmega32U4)

End of Document — ARES-NAV Complete Technical Specification Rev. 2.5 | Duwald Systems